## Slide 1: Unit – 1: Introduction
Prof. Maulik Trivedi
 9998265805
 maulik.trivedi@darshan.ac.in
Computer Engineering | Darshan Institute of Engineering & Technology
Mobile Computing and Wireless Communication (2170710)

## Slide 2: Outline
Introduction
Mobile Computing & Wireless Communication
Transmission Media
Multiplexing (Covered in Unit - 2)
LANs, MANs, and WANs
Switching Techniques
The OSI Model
The TCP/IP Protocol Architecture

## Slide 3: Introduction
Mobile Computing is a technology that allows transmission of data, voice and video via a computer or any other wireless enabled device without having to be connected to a fixed physical link.
The main concept involves:
  Mobile communication
  Mobile hardware
  Mobile software
Mobile communication refers to the infrastructure put in place to ensure that seamless and reliable communication goes on.
These would include devices such as protocols, services, bandwidth, and portals necessary to facilitate and support the stated services.

## Slide 4: Introduction – Cont…
Mobile hardware includes mobile devices or device components that receive or access the service of mobility.
They would range from portable laptops, smartphones, tablet Pc's, Personal Digital Assistants.
Mobile software is the actual program that runs on the mobile hardware.
In other terms, it is the operating system of the appliance. It's the essential component that operates the mobile device.

## Slide 5: Mobile Computing
Different names of mobile computing:
  VHE – Virtual Home Environment
  Anywhere, anytime information
  Nomadic computing
  Pervasive computing
  Ubiquitous computing
  Global service portability
  Wearable computers
  Context aware computing
Attribute of Mobility
  Network Mobility
  Bearer Mobility
  Device Mobility
  Session Mobility
  Service Mobility
  Host Mobility
  User Mobility

## Slide 6: Limitation of Mobile Computing
Limitations of the wireless network
  Heterogeneity of fragmented networks
  Frequent disconnections
  Limited communication bandwidth
Limitations imposed by mobility
  Lack of mobility awareness by system / applications
  Route breakages
Limitations of the mobile computer
  Short battery lifetime
  Limited capacities (memory, processing speed, etc.)

## Slide 7: Wireless Communication
Wireless communication involves the transmission of information over a distance without the help of wires, cables or any other forms of electrical conductors.
It is a broad term that incorporates all procedures and forms of connecting and communicating between two or more devices using a wireless signal through wireless communication technologies and devices.

## Slide 8: Wireless Communication – Cont…
The transmitted distance can be anywhere between a few meters (for example, a television's remote control) and thousands of kilometers (for example, radio communication).
Wireless communication can be used for cellular telephony, wireless access to the internet, wireless home networking, and so on.
Examples of applications of wireless technology include
  GPS Units
  Garage Door Openers
  Wireless keyboard-mouse
  Headsets
  Radio Receivers
  Satellite Television
  Broadcast Television
  Cordless Telephones

## Slide 9: Advantages
Cost effectiveness
Flexibility
Convenience
Speed
Accessibility
Constant Connectivity

## Slide 10: Application & Services
There are six basic categories:
Personal (wallet, diary, etc.)
Perishable (news, sports, stock quotes, etc.)
Transaction oriented (bank transactions, mobile shopping, etc.)
Location specific (restaurant guide, map service, etc.)
Corporate (ERP, inventory, business alerts, etc.)
Entertainment (fun, games, etc.)

## Slide 11: Transmission Media
A transmission media can be defined as any medium that can carry information from a source to a destination.
Transmission Media
Guided Media (Wired)
Unguided Media (Wireless)
Twisted-Pair Cable
Coaxial Cable
Fiber Optic Cable
Radio Wave
Microwave
Infrared Wave

## Slide 12: Guided Media
Guided media are those that provide a wired - channel from one device to another.
Three Guided media commonly used for data transmission are:
  Twisted Pair Cable
  Coaxial Cable
  Fiber Optic Cable

## Slide 13: Twisted Pair Cable
Separately insulated
Twisted together
Two types of twisted pair cable
UTP(Unshielded Twisted Pair)
  Ordinary telephone wired
  Less expensive
  Weak immunity against noise & interferences
  Most used in two categories: Cat-3 & Cat-5
STP(Shielded Twisted Pair)
  An extra metallic shield on each pair
  Relatively more expensive
  Better performance than UTP

## Slide 14: Coaxial Cable
Outer conductor is braided shield
Inner conductor is solid metal
Separated by insulating material
Used in television, long distance telephone transmission
High bandwidth and excellent noise immunity

## Slide 15: Fiber Optic Cable
Glass or plastic core
Laser or light emitting diode
Small size & weight
Used in high bandwidth network
High data rate & lower attenuation

## Slide 16: Unguided Media
Unguided media transmit electromagnetic waves without using a physical conductor.
This type of communication is often referred to as wireless communication.
  Radio wave
  Microwave
  Infrared Wave

## Slide 17: Radio wave
Highly regulated
Omni directional antennas
Radio waves are used for multicast communications, such as radio and television, and paging systems
Penetrate through walls

## Slide 18: Microwave
Use directional antennas - point to point line of sight communications
Microwave communication
Used for unicast communication such as cellular telephones, satellite networks
Higher frequency ranges cannot penetrate walls

## Slide 19: Infrared wave
Infrared signals can be used for short-range communication in a closed area using line-of-sight propagation
Used on televisions, VCRs, and stereos all use infrared communication.
Relatively directional
Cheap, Easy to build but they do not pass through solid objects

## Slide 20: Communication Network
Communication networks can be categories by their size as well as their purpose.
The size of a network can be expressed by the geographic area.
Some of the different networks based on size are:
    LAN – Local Area Network
    MAN – Metropolitan Area Network
    WAN – Wide Area Network

## Slide 21: Local Area Network
A local area network (LAN) is a computer network that interconnects computers within a limited area such as a residence, school, laboratory, university campus or office building.

## Slide 22: Metropolitan Area Network
A metropolitan area network (MAN) is a computer network that interconnects with computer in a metropolitan area like city.
MAN is a larger than LAN but smaller than the area covered by a WAN.
It is also used to interconnection of several local area network.
Navagam
Shapar
Morbi
Rajkot

## Slide 23: Wide Area Network
A wide area network (WAN) is a computer network that exists over a large-scale geographical area.
A WAN connects different networks, including local area networks (LAN) and metropolitan area networks (MAN).
It may be located with in a state or a country or it may be interconnected around the world.

## Slide 24: Types of Computer Networks
Basis Of Comparison | LAN | MAN | WAN
Full Name | Local Area Network | Metropolitan Area Network | Wide Area Network
Meaning | A network that connects a group of computers in a small geographical area | It covers relatively large region such as cities, towns | It spans large locality & connects countries together. e.g. Internet
Ownership of Network | Private | Private or Public | Private or Public (VPN)
Design and Maintenance | Easy | Difficult | Difficult
Propagation Delay | Short | Moderate | Long
Speed | High | Moderate | Low
Equipment Used | NIC, Switch, Hub | Modem, Router | Microwave, Radio Transmitter & Receiver
Range(Approximately) | 1 to 10 km | 10 to 100 km | Beyond 100 km
Used for | College, School, Hospital | Small towns, City | State, Country, Continent

## Slide 25: Switching
Defines the connection of different network segments together and the process to transmit the data packets across the network.
It is implemented through the use of switching techniques.
Switched
Networks
Packet-Switched
Networks
Circuit-Switched
Networks

## Slide 26: Circuit Switched Network
A dedicated channel has to be established before the call is made between users.
The channel is reserved between the users till the connection is active.
For half duplex(one way) communication, one channel is allocated and for full duplex(two way) communication, two channels are allocated.
It is mainly used for voice communication requiring real time services without delay.

## Slide 27: Packet Switched Network
It is not required to establish the connection initially.
The connection/channel is available to use by users. But when traffic or number of users increases then it will lead to congestion in the network.
Packet switched networks are mainly used for data and voice applications requiring non-real time scenarios.

## Slide 28: Differences
Circuit Switching | Packet Switching
Dedicated path between source and destination | No dedicated path
All packets use same path | Packets travel independently
Reserve the entire bandwidth in advance | Does not reserve bandwidth
Bandwidth wastage | No bandwidth wastage
No store and forward transmission | Supports store and forward transmission

## Slide 29: Switching Network

## Slide 30: Protocol Layers

## Slide 31: What is Protocol?
Human Protocol(Language)
  “what’s the time?”
  “I have a question”
  Introduction Talk
Network Protocol
  Set of rules
  machines rather than humans
  all communication activity in Internet governed by protocols.
  Protocols define format, order of message sent and received among network entities, and actions taken on message transmission and receipt

## Slide 32: Protocols Layers
To deals with connecting systems that are open for communication with other systems.
OSI Layer Model (Open Systems Interconnection)
Developed by the International Standards Organization (ISO) with seven different layers.
    Physical Layer
    Data Link Layer
    Network Layer
    Transport Layer
    Session Layer
    Presentation Layer
    Application Layer

## Slide 33: Example – Air Plane Travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departure
Arrival

## Slide 34: How OSI Layer Works?

## Slide 35: Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 36: Data Link Layer
The data link layer is responsible for moving frames from one hop (node) to the next.

## Slide 37: Network Layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 38: Transport Layer
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 39: Session Layer
The session layer is responsible for dialog control and synchronization.

## Slide 40: Presentation Layer
The presentation layer is responsible for translation, compression, and encryption.

## Slide 41: Application Layer
The application layer is responsible for providing services to the user.

## Slide 42: Summary – OSI Layer
Application
Presentation
Session
Transport
Network
Data link
Physical
To allow access to network resource
To translate, encrypt and compress data
To provide reliable process-to-process message delivery and error recovery
To establish, manage and terminate sessions
To move packets from source to destination; To provide internetworking
To transmit bits over a medium; To provide mechanical & electrical specification
To organize bits into frames; To provide hop-to-hop delivery

## Slide 43: TCP/IP Reference Model (Transmission Control Protocol/Internet Protocol)
It was originally defined as having five layers:
TCP/IP is a set of protocols developed to allow cooperating computers to share resources across the network.
  Application Layer
  Transport Layer
  Network Layer
  Data Link Layer
  Physical Network

## Slide 44: TCP/IP Model Architecture

## Slide 45: Difference
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol/ Internet Protocol)
OSI provides layer functioning and also defines functions of all the layers | TCP/IP model is more based on protocols and protocols are not flexible with other layers
In OSI model the transport layer guarantees the delivery of packets | In TCP/IP model the transport layer does not guarantees delivery of packets
Follows horizontal approach | Follows vertical approach
OSI model has a separate presentation layer | TCP/IP doesn’t have a separate presentation layer
OSI is a general model | TCP/IP model cannot be used in any other application

## Slide 46: Difference - Cont…
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol/ Internet Protocol)
Network layer of OSI model provide both connection oriented and connectionless service | The Network layer in TCP/IP model provides connectionless service
OSI model has a problem of fitting the protocols in the model | TCP/IP model does not fit any protocol
Protocols are hidden in OSI model and are easily replaced as the technology changes | In TCP/IP, replacing protocol is not easy
OSI model defines services, interfaces and protocols very clearly and makes clear distinction between them | In TCP/IP, it is not clearly separated its services, interfaces and protocols
It has 7 layers | It has 5 layers

## Slide 47: Summary
Signals for Conveying Information (Analog and Digital Signal)
Analog and Digital Data Transmission (Continue, Discrete)
Channel Capacity (Bandwidth, Data Rate, Noise, Error Rate)
Transmission Media (Cables)
LANs, MANs, and WANs
Switching Techniques (Circuit and Packet Switching)
The OSI Model (Seven Layers)
The TCP/IP Protocol Architecture (Protocols)

## Slide 48: Thank You